## Slide 1: Wetland Carbon Stocks Under Forest Canopy: GDA 599
Anthony J. Stewart1, Meghan Halabisky1, Chad Babcock2, David Butman1, David D'Amore3, L. Monika Moskal1
1University of Washington, 2University of Minnesota, 3USDA Forest Service
Thanks to Thomas Kakatsakis
Traditional Lands of the Hoh and Quinault Tribes

## Slide 2: Background: Wetland Identification
DEM Metrics:
Slope, Depression Area, Topographic Wetness Index
LiDAR
Where does water pool?
Random Forest
Algorithm*
Dr. Meghan Halabisky*
LiDAR Digital Elevation Model
National Wetland Inventory Training Data
Wetland/Upland
Landscape pixels
Slope
TWI
Curve
Landscape pixels
Dep
Curve
TWI
Hoh Watershed

## Slide 3: Wetland and their Carbon
Anoxic conditions from water saturation slow decomposition
Wetlands store 20-30% of global soil carbon despite occupying only 5-8% of the land surface

## Slide 4: Background: Carbon Measurements
Objective: Apply these carbon stock measurements to the entire watershed
Hoh River Watershed
Thomas Kakatsakis

## Slide 5: Methods
Data sources
  SRTM 1 ArcSec (~30m) DEM
    Use OpenTopography API to extract with bounds
  Shapefile of Hoh Watershed from collaborator
Open Data with rasterio
Reproject to EPSG:32610
Clip to Hoh Watershed shapefile

## Slide 6: Methods – Generating Wetland Probability
Use some ArcGIS black magic
  Makes topography metrics
  Water flow routing
  Random Forest
https://github.com/DanMillerM2/ForestedWetlands
Wetland Intrinsic Probability = WIP

## Slide 7: Methods – Back to Python
Import more raster data layers
  Topographic Wetness Index
  Contributing Catchment Area
  Slope
Import Carbon point data as geodataframe
Sample each raster (WIP, TWI, CatArea, Slp) with Rasterio and attach to geodataframe
Analyze with Multiple Linear Regression
Multiply coefficients by corresponding rasters

## Slide 8: Results – What?
wip, catarea, twi, slp, intercept = [-5.6060e+00 -1.5000e-02 4.2390e+00 4.3230e+00 -2.2714e+01]
KgC/m2
All Variables Sampled (WIP, TWI, CatArea, Slp)

## Slide 9: Results- Better?
All Variables with vmin = 0
KgC/m2
np.nansum(MLR[MLR>0]) = 1,050,141.1 KgC

## Slide 10: Results Even Better?
No WIP
No CatArea
KgC/m2
KgC/m2

## Slide 11: Discussion
Changes to make things better
  Use rioxarray instead of rasterio
  Use alternative raster sampling methods
  Figure out better relationships with catchment area
  Include water features such as rivers, mountains to mask out potential areas